## Slide 1: EVALUATING THE PERFORMANCE OF COMPLEX HYPERDIMENSIONAL COMPUTING ON RASPBERRY PI AND GOOGLE COLAB-GPU USING THE MNIST DATASET
ECE 618: Hardware Accelerators for Machine Learning
Raja Kumar Janga - G01411489
Rohith Kumar Kalisetti – G01410445

## Slide 2: CONTENTS
Introduction
What is HDC?
Methodology
Experimental Setup – Baseline
Workflow
Code Analysis
Experimental Setup – Raspberry pi
Code Analysis
Optimization
Result Overview
Baseline Result
Edge Device Results
Analysis
Future Work
Conclusion

## Slide 3: Introduction
Hyperdimensional Computing (HDC) offers an alternative to traditional ML by leveraging high-dimensional vectors for robust and efficient computation.
This project compares HDC performance on:
Raspberry Pi (low-cost, resource-limited)
Google Colab (GPU-enabled environment)
Objective: Evaluate Training Time, Testing Time, Memory Usage, and Accuracy.

## Slide 4: What is Hyperdimensional Computing (HDC)?
Hyperdimensional Computing (HDC) is an alternative computational model inspired by the way the human brain processes information. It operates on high-dimensional vectors, which represent data overall.
Key Features:
- Robustness to noise and errors.
- Efficient and lightweight compared to traditional machine learning algorithms.
- Suitable for hardware-constrained environments like Raspberry Pi.
Applications:
- Cognitive computing.
- Pattern recognition and classification.
- Low-power, embedded systems.

## Slide 5: Methodology
Dataset: MNIST (handwritten digit classification)
Model: HDC (Hyperdimensional Computing)
Platforms:
- Raspberry Pi (D=5000, CPU)
- Google Colab (D=10000, GPU)
Metrics Evaluated:
- Training Time
- Testing Time
- Memory Usage
- Accuracy

## Slide 6: Methodology

## Slide 7: Experimental Setup - Baseline
Focus: Leveraging GPU for faster computation.
Preprocess MNIST dataset.
GPU: NVIDIA Tesla T4
Memory: 16 GB
Use DIMENSIONS = 10000 to utilize GPU capabilities.
Set optimized batch size for parallel processing.
Train the HDC model using GPU.

## Slide 8: Experimental Setup - Baseline
Pre-Process Data Set: MNIST
70,000 hand-written images of the digits, 0-9
Stored as 28x28 byte grayscale images with their associated labels

## Slide 9: Workflow
Encoding Hypervectors:
Position Embedding:
  Assigns unique position hypervectors to each pixel using embeddings.Random.
  Generates random hypervectors for the 28x28 grid.
Value Embedding:
  Quantizes pixel intensities into discrete levels (e.g., NUM_LEVELS =1000).
  Maps these levels to hypervectors using embeddings.Level.
Binding Operation:
  Combines position and value hypervectors using torchhd.bind, creating unique hypervectors that encode both pixel position and intensity.
Multiset Operation:
  Aggregates all bound hypervectors into a single high-dimensional hypervector using torchhd.multiset for compact representation.

## Slide 10: Encoding

## Slide 11: Training

## Slide 12: Experimental Setup – Raspberry Pi
Focus: Implementing HDC on a resource-constrained device.
Preprocess MNIST dataset.
CPU: ARM Cortex-A72
Memory: 4 GB
OS: Debian-based Raspberry Pi OS
Use DIMENSIONS = 5000 for memory efficiency.
Set batch size to 1 to fit into limited RAM.
Train the HDC model using CPU.

## Slide 13: Encoding

## Slide 14: Training

## Slide 15: Optimization
Hard Quantization Optimization:
Replaced the deprecated torchhd.hard_quantize with the recommended torchhd.normalize for robust vector processing.
Converts high-dimensional vectors into binary states (+1 or -1), simplifying computation.
Improves model compatibility with the latest libraries and ensures stable performance.

## Slide 16: Optimization
Dimensionality Adjustment:
Raspberry Pi: Reduced dimensionality (DIMENSIONS = 5000) to minimize memory usage and computation requirements.
Google Colab: Increased dimensionality (DIMENSIONS = 10000) to fully utilize GPU capabilities and improve accuracy.
Model Efficiency:
Lightwieght centroid-based HDC model avoids the complexity of traditional deep learning architectures.
Encoders effieciently bind and qunatize data into hyperdimensional vectors, ensuring computationally simplicity.

## Slide 17: Results Overview
Metrics | Raspberry Pi | Google Colab
Training Time (s) | 1741 | 96.61
Testing Time (s) | 316 | 20.78
Memory Usage (MB) | 496 | 205
Accuracy (%) | 82.75 | 82.99

## Slide 18: Baseline results

## Slide 19: Raspberry pi results

## Slide 20: Accuracy and Timing Analysis

## Slide 21: Memory Comparison

## Slide 22: Future Work
Dataset Expansion:
Test on more complex datasets to evaluate scalability and accuracy (e.g., CIFAR-10, Tiny ImageNet).
Algorithm Improvements:
Enhance encoding mechanisms for higher precision and lower dimensionality.
Hardware Acceleration:
Develop FPGA/ASIC implementations for faster and more energy-efficient performance.
Hybrid Models:
Combine HDC with neural networks to create hybrid models leveraging the strengths of both paradigms.
Integration in Real-Time Systems:
Apply the method to real-time applications like handwriting recognition, gesture classification, or autonomous navigation.

## Slide 23: Conclusion
This project highlights the adaptability of HDC and its potential in both edge and cloud computing environments.
Google Colab is optimal for time-sensitive tasks.
Raspberry Pi is suitable for cost-effective, offline experiments.
Binary representation makes the system ideal for hardware implementations, such as FPGA or ASIC accelerators.

## Slide 24: THANK YOU